## Slide 1
Networking Infrastructure
Ethernet Switching - Spanning Tree Protocol
& Ethernet Evolution
Lecture
NI
2
Networking Infrastructure
Diploma in CSF / IT
Year 2 (April 2022), Semester 3
Notes: Left-hand Bar – Replace FSP by your module code and X by the lecture number.
Replace Lecture Title
Replace < Module Name >
Replace Year and Semester if necessary

## Slide 2
Layer 2 switching operations
Switching modes
Redundancy in switch topologies
Spanning Tree Protocol
Evolution of Ethernet Technologies: Fast & Gigabit Ethernet (optional)
Objectives :

## Slide 3
Address Learning (Recap)
Flooding (Recap)
Forward (Recap)
Filter Decision
Aging
Layer 2 Switching Operations

## Slide 4
Layer 2 Switching – Address Learning
Switch
1
2
3
4
A
B
C
D
E
Interfaces/Ports
Stations
MAC Address Table
Data from A to B
1 2 3 4
A
Learns the source MAC address of each
data frame that is transmitted and noting the port where the frame enters the switch

## Slide 5
Layer 2 Switching – Flooding
4
B
Switch
1
2
3
A
C
D
E
MAC Address Table
Interfaces/Ports
Stations
1 2 3 4
A
Data from A to B
Data from A to B
Data from A to B
Sends out on all ports (except the port that the frame entered from) when the destination MAC address is unknown (not in Table) or a broadcast (no need to refer to Table)

## Slide 6
Layer 2 Switching – Forwarding
B
Learns the source MAC address of each
data frame that is transmitted and noting the port where the frame enters the switch
Switch
1
2
3
4
A
B
C
D
E
Interfaces/Ports
Stations
MAC Address Table
1 2 3 4
A
Data from B to A
Forwards when the
destination MAC matches an entry in the Table
Data from B to A

## Slide 7
Layer 2 Switching – Filtering
Data from A to C
Switch
1
2
3
4
A
B
C
D
E
Interfaces/Ports
Stations
MAC Address Table
1 2 3 4
A
B
C
D
E
Filters when the destination
is located on the same port (both A & C are under port 3 in the Table)

## Slide 8
If the destination address is unknown to the switch, it forwards the frame to all segments except the one on which it was received
  this process is known as flooding
If the destination device is on a different segment, the switch forwards the frame to the appropriate segment
  this process is known as forwarding
If the destination device is on the same segment as the frame, the switch blocks the frame from going on to other segments
  this process is known as filtering
Layer 2 Switching Operations
Notes: An ethernet switch is a multiport ethernet bridge. A bridge is a device that splits collision domains but not broadcast domains.
A switch is simply a bridge with lots of ports.
Note: some wireless router may be configured as a bridge (without routing).

## Slide 9
How a Switch populates MAC address table and performs Aging of entries
Learns the MAC address of each device on the network
  reads the source MAC address of each data frame that is transmitted and noting the port where the frame entered the switch
Addresses are learnt dynamically and added to the MAC Address Table (or switching table)
  address is time stamped
  address is stored for a set period of time – Age Time (default 300 sec)
  addresses that are not referenced beyond the Age Time are removed - Aging
  maintains an accurate and functional table by removing aged addresses
Layer 2 Switching Operations

## Slide 10
How the contents of a frame is switched to the destination port?
Three switching modes {offering different performance & latency } :
  Store-and-Forward Switching
  Cut-Through Switching
  Fragment-Free Switching
Switching Modes
Switching Modes

## Slide 11
Switching Modes
Switch
Source
Destination
DA
SA
Type
Data
FCS
Checked the frame. It is good (FCS). I am to forward the frame now.
Store-and-Forward Switching

## Slide 12
Read the entire frame into memory buffer & determine whether the frame is valid or invalid.
  Fragment less than 64 bytes due to collision.
  Corrupted frame detected using the FCS field.
Advantage: prevents wasting the bandwidth on the destination network by invalid or bad frames that can adversely affect the network performance.
Downside: the frame error checking and memory buffering contributes to greater delay or latency.
Store-and-Forward Switching

## Slide 13
Switching Modes
Switch
Source
Destination
DA
SA
Type
Data
FCS
I have the destination MAC address (DA). I can transmit the frame now.
Cut-Through Switching

## Slide 14
sometimes referred to as fast forward switching or on-the-fly switching.
Reads the beginning of the frame up to the destination MAC address field in the data frame as the traffic flows through the switch.
Does not wait for the entire data frame to be read in before switching the frame to the destination port i.e. “cut-through” .
Advantage: fast and minimum latency; requires less buffer memory
Downside: lacks frame error checking; forwards corrupted frame and fragments and could congest the network traffic with unwanted invalid frames (when traffic levels increase, as more errors are more likely to occur)
Cut-Through Switching

## Slide 15
Switching Modes
Switch
Source
Destination
DA
SA
Type
Data
FCS
I have received the 1st 64 bytes (min Eth frame size). I can transmit now.
Fragment-Free Switching
1st 64 bytes

## Slide 16
Frames are buffered until the first 64 bytes have been received
Can check for any bad frames (fragments less than 64 bytes due to collisions) but will not be able to detect frames with FCS errors.
Results in lesser latency (compared to store-and-forward) as the frame is sent after it has read 64 bytes.
Fragment-Free Switching

## Slide 17
Modes
Advantages
Cut-through
Very fast =>
Low constant latency
Fragment-Free
Filters out fragments
Switching Modes Summary
Disadvantages
Store-and-Forward
No bad frames
“Latency” to read
whole frame - varies
Forward fragments &
error frames
Forward error frames

## Slide 18
Store-and-forward switching mode
  Reads and check whole frame before forwarding
  Advantage: No invalid frames forwarded
  Disadvantage: Variable latency (delay in switch)
Cut-Through switching mode
  Reads and check destination address only before forwarding
  Advantage: Low constant latency
  Disadvantage: Fragments and error frames forwarded
Fragment-Free switching mode
  Reads and checks first 64 bytes of frame only before forwarding
  Advantage: No frames less than 64 bytes long are forwarded
  Disadvantage: Error frames forwarded
Switching Modes Summary

## Slide 19
Resilience (using redundancy) with multiple switches and trunk links
One link or device fails – another takes over.
We want achieve:

## Slide 20
Problems with redundancy
Switching loops give problems if all the links are active:
Broadcast storms
Multiple frame transmission
Inconsistent switch tables

## Slide 21
Send ARP request
There’s a switching loop
Flood broadcast through non-source ports
And so on with nothing to stop it
Broadcast Storm

## Slide 22: Multiple Frame Transmissions
A
B
Send frame to B
A is on port 3
Don’t know B
So flood
Frame arrives
And again

## Slide 23: Inconsistent switch tables
A
B
Send frame to B
A is on port 3
Don’t know B
So flood
A is on port 1
A is on port 2
???
A is on port 3
A is on port 1
A is on port 2
?

## Slide 24: Redundancy without loops
There needs to be just one path at a time.
Redundant paths must be shut down, but ready to be opened when they are needed.
This must be done quickly and automatically.
Spanning Tree Protocol does this.

## Slide 25: What is a spanning tree?
A tree (extended star) topology
  A tree has no loops
Spanning all devices
  All devices are connected

## Slide 26: Not a spanning tree
There are loops.

## Slide 27: Not a spanning tree
Device left out.

## Slide 28: Spanning tree
No loops. Includes all devices.

## Slide 29: Spanning tree protocol
Used by switches to turn a redundant topology into a spanning tree
Disables unwanted links by blocking ports
STP defined by IEEE 802.1d
Rapid STP defined by IEEE 802.1w
Switches run STP by default – no configuration needed.

## Slide 30: Spanning tree algorithm
The switches use this algorithm to decide which ports should be shut down.
Select one switch to be “root bridge”
Select a “root port” on each other switch
Select a “designated port” on each segment.
Close down all other redundant ports/links.

## Slide 31: Outline of process
Root bridge
Root port
Root port
Root port
Designated port
Designated port
Designated port
Designated port
Not chosen Block/Close down

## Slide 32: 1 Select the root bridge
Each switch has a bridge ID (BID) of priority value followed by MAC address
Switches exchange Bridge Protocol Data Units (BPDUs) to compare bridge IDs
The switch with the lowest bridge ID becomes the root bridge
Administrator can set the priority to fix the selection

## Slide 33: 1 Select the root bridge
The bridge ID consists of bridge priority, extended system ID, and MAC address
By default the priority is 32768
Lowest priority wins
Value 1 - 65536, multiples of 4096
Extended system ID identifies VLAN.
MAC address used if priority is the same. Better not to rely on MAC address.

## Slide 34: 1 Select the root bridge
A switch starts up. It sends out BPDU frames containing the switch Bridge ID (BID) and the root ID every 2 seconds.
At first each switch identifies itself as the root bridge.
If a switch receives a BPDU with a lower BID then it identifies the switch with that BID as root bridge. It passes on this information in its own BPDUs.
Eventually all switches agree that the switch with the lowest BID is the root bridge.

## Slide 35: 2. Select root ports
Every non-root bridge/Switch selects a root port
This is the port with the shortest distance / lowest cost path to the root bridge/switch
If same distance, use the one with lowest ID
Notes: From Root Port to Designated Port

## Slide 36: 3. Select designated ports
On every segment, the port with the lowest cost path to the root bridge becomes the designated port

## Slide 37: Designated port if same distance/cost
Choose the port on the switch with the lower bridge ID. Suppose this is switch B.

## Slide 38: 4. Close down all redundant links/ports
Any port that is not a root port or a designated port is put in blocking state

## Slide 39
Spanning Tree Protocol (STP) is a Layer 2 link-management protocol that provides path redundancy while preventing undesirable loops
A loop-free topology is accomplished when the switch recognizes a loop in the topology and logically blocks one or more redundant ports automatically
Bridge Protocol Data Units (BPDUs) are used by switches in a network to exchange information regarding their status
The switches use the Spanning Tree Algorithm (STA) to resolve and shutdown redundant paths
STP is defined in the IEEE 802.1d specification
Spanning Tree Overview

## Slide 40
Redundant Paths is good for network resilience
Broadcast Storms caused by redundant paths
Spanning Tree Protocol (STP) overcomes broadcast storms by using Loop Avoidance
  Redundant paths are blocked (made inactive)
  Only one active path between any node (e.g. PC) in the network
  Should active path fail, blocked path is activated automatically
  Hence network resilience is achieved without broadcast storms
Spanning Tree Protocol Summary

## Slide 41
First proposed in 1973
First tested in 1976: 3 Mbps
First standardized in 1980: 10 Mbps
Wireless (802.11b) in 2000: 11 Mbps
Currently being developed: 100Gbps
Bit rates and signal encoding (Layer 1) differ among the main versions
The frame structure (Layer 2) remains more or less the same
CSMA/CD & Half Duplex (Layer 2) not supported from 10Gigabit Ethernet upwards
Evolution of Ethernet (Optional)

## Slide 42
Types of Ethernet
Logical link Control Sublayer
802.3 Media Access Control (MAC)
10BASE5 (500m)
50 Ohm Coax N-Style
10BASE2 (185m)
50 Ohm Coax BNC
10BASE-T (100m)
100 Ohm UTP RJ45
100BASE-TX (100m)
100 Ohm UTP RJ45
100BASE-FX (228-412m)
MM Fiber SC
1000BASE-T (100m)
100 Ohm UTP RJ45
1000Base-SX (220-550m)
MM Fiber SC
1000Base-LX (550-5000m)
MM Fiber SC
10GBase-(Various)
MM or SM Fiber SC
Physical
Signalling
Sublayer
Physical
Medium

## Slide 43
Legacy Ethernet – 10Mbps
10BASE5
Thicknet
“Original”
1980
50 Ohm Thick Coaxial N Style
500m
Type
Standard
Cabling Type
Distance
10BASE2
Thinnet
50 Ohm Thin Coaxial BNC
185m
802.3a-
1985
10BASE-T
100 Ohm UTP RJ45
100m
802.3i-
1990

## Slide 44
Fast Ethernet – 100Mbps
Type
Standard
Cabling Type
Distance
100BASE-FX
Multimode Fiber Optic
412m
802.3u-
1995
100BASE-TX
802.3u-
1995
100m
100 Ohm UTP RJ45
Two pairs of twisted-pair
100Base-TX
Implementation
100Base-FX
Implementation

## Slide 45
Gigabit Ethernet – 1000Mbps or 1Gbps
Type
Standard
Cabling Type
Distance
1000BASE-T
100 Ohm UTP RJ45
100m
802.3ab-
1999
Medium Modal Bandwidth
1000BASE-SX
802.3z-
1998
62.5um MMF 160 MHz/km 220m
62.5um MMF 200 MHz/km 275m
50um MMF 400 MHz/km 500m
50um MMF 500 MHz/km 550m
1000BASE-LX
802.3z-
1998
62.5um MMF 500 MHz/km 550m
50um MMF 400 MHz/km 550m
50um MMF 500 MHz/km 550m
10um SMF - 5000m

## Slide 46
1000Base-X Implementation
Two fiber-optic cables
Short wavelength (SX)
Long wavelength (LX)
1000Base-T Implementation
Uses at least Cat 5 UTP
Four twisted pairs
Gigabit Ethernet – 1000Mbps or 1Gbps
Notes: Cat 5 and 5e UTP cables are no longer available in the market

## Slide 47
10 Gigabit Ethernet
10GBASE-SR
Short distances over 62.5µm MMF,
range from 26 – 82m. Over 50 µm, range 300m
10GBASE-LX4
300m over 62.5µm MMF, 10km over SMF
10GBASE-LR
10GBASE-ER
LR supports 10km,
ER supports 40km over SMF
10GBASE-SW
10GBASE-LW
10GBASE-EW
Intended to work with OC-192STM SONET/ SDH
WAN equipment
10GBASE-T
100m, at least Cat 6a UTP
2006
2002
2002
2002
2006

## Slide 48
1Gbps is widely used
10Gbps used for server and backbone connections
40Gbps currently available
100Gbps is emerging
160Gbps wired and 640 Mbps wireless in future(?)
Networking Media likely to remain
  Copper
  Optical fiber
  Wireless
Ethernet Trends

## Slide 49
Layer 2 switching operations
Switching modes
  Store-and-Forward Switching
  Cut-Through Switching
  Fragment-Free Switching
Redundancy in switch topologies
Spanning Tree Protocol
  Root bridge/switch
  Root port
  Designated port
  Block port
Summary